## Slide 1: A Formulation for Unknown Focal Length
Changchang wu
Google

## Slide 2: Directly Solving for Focal Length?
There is a two fold redundancy
Leads to 2X solutions, and slower minimal solver
The problem exists in both absolute pose and relative pose
Negated focal length
additional rotation around z by 180

## Slide 3: Getting Around such Redundancies?
Sometimes there is a pattern of f^2
  Relative pose with unknown focal length
Modeling the problems differently
  Absolute pose with unknown focal length (P4P)
    3D Point distance (ratio) -> over-determined
    Null space -> not general
Sometimes you are unlucky
  Absolute pose with one also unknown radial distortion
12 meaningful solutions out of 24 in Josephson et al. CVPR 2009

## Slide 4: A New Parameterization
Separate the rotation around the Z axis
Combine the rotation around the Z axis with focal length
The same number of parameters (Dof) without the redundancy
Possible degeneracy with f = 0 (any θ ) is reduced to (fc = fs = 0)

## Slide 5: Application : P4P -> P3.5P (Wu CVPR 2015)
Truly minimal (using exactly 7 coordinates)
  Allows to work with single coordinates
  Exactly the minimal 10 solution
  Extra coordinate can be used for solution filtering
Simpler polynomial system & faster GB solver

## Slide 6: Other Applications
Relative pose between generalized camera and uncalibrated pinhole
  See our “Structure-less resection” poster at 3A-1
  Reduces the number of solutions by half (e.g. 100->50 for 5+2)
Feels like symmetry?
Absolute pose with unknown focal length & radial distortion
  Reduces the number of solutions from 24 to 12
  Using a different radial distortion model.

## Slide 7
Thank you!